Safe Work Method Statement

Organisation: Sample

Task: Whipper Snipping

Task objective: To safely trim grass

Hazards Hazards associated with entanglement, impact and cutting injuries, shearing, ergonomics, noise, slips and trips, uv exposure, fire and explosion and petrol fumes.

Tools and PPE: Gloves Hearing protection Eye protection Appropriate clothing Appropriate footwear Hat and sunscreen

| Training and instruction: Manual handling Correct use of PPE Hearing protection UV protection Manufacturers operating instructions |
| --- |
| Steps |
| Prior to procedure: Make sure equipment is free of any signs of wear or damage. Check guards ensuring they are in working order. Operator to inspect work area to ensure that work surface is even and stable to prevent slips, trips and falls. Wear the appropriate PPE. Fuel whipper snipper away from any possible sources of ignition. Always turn off whipper snipper before replacing line. Adjust harness and handle length so able to maintain an upright posture with elbows slightly bent |
| During procedure: Keep hands, feet and loose clothing away from all moving parts. Do not overreach and ensure proper footing and balance. Avoid using above knee level Never leave whipper snipper running unattended. Ensure moving parts have come to a complete stop before performing any maintenance or cleaning. Make sure motor is stopped and allowed to cool before refuelling. Refuel only in a well-ventilated area away from possible ignition sources. |
| Post procedure: Ensure moving arts have completely stopped before storing. Ensure equipment is returned to storage area after use. |
| Precautions: PPE must be worn at all times Always operate with 2 hands Avoid operating above knee level Ensure muffler exhaust is away from the body Use a shoulder strap to reduced strain with prolonged use Follow safe use instructions at all time |
| Read by: | Signed: | Date: |